## Slide 1: Routing Information Protocol(RIP) AND Open Shortest Path First(OSPF)
Sujina Maharjan

## Slide 2: Routing Information Protocol (RIP)
A dynamic protocol used to find the best route or path from end-to-end (source to destination) over a network.
Prevents routing loops by implementing a limit on the number of hops allowed in a path from source to destination.
The maximum number of hops allowed for RIP is 15, which limits the size of networks that RIP can support.
uses a routing metric/hop count algorithm which is used to determine the shortest path from the source to destination.

## Slide 3: Cont.……
The hop is the step towards the next existing device, which could be a router, computer or other device.
Once the length of the hop is determined, the information is stored in a routing table for future use.
used in both local and wide area networks and is generally considered to be easily configured and implemented.
Comparing to OSPF and others RIP is not considered as protocol with good scalable and convergence.

## Slide 4: Versions Of RIP
RIP version1
RIP Version2
was published in 1988 and uses classful routing.
The periodic routing updates do not carry subnet information,
was developed in 1993 and last standardized in 1998.
It included the ability to carry subnet information,

## Slide 5: Limitations
The hop count cannot exceed 15, or routes will be dropped.
Most RIP networks are flat. There is no concept of areas or boundaries in RIP networks.
Variable Length Subnet Masks are not supported by RIP version 1 (which is obsolete).
RIP has slow convergence and count to infinity problems.

## Slide 6: Open Shortest Path First OSPF
a routing protocol for Internet Protocol (IP) networks.
It uses a link state routing algorithm and falls into the group of interior routing protocols, operating within a single autonomous system (AS).
OSPF is an interior gateway protocol (IGP) for routing Internet Protocol (IP) packets solely within a single routing domain.

## Slide 7: Cont.….
It gathers link state information from available routers and constructs a topology map of the network.
OSPF supports Internet Protocol Version 4 (IPv4) and Internet Protocol Version 6 (IPv6) networks.
features both variable-length subnet masking (VLSM) and Classless Inter-Domain Routing (CIDR) addressing models.

## Slide 8: Difference between RIP and OSPD
The main difference between OSPF and RIP is that RIP only keeps track of the closest router for each destination address, while OSPF keeps track of a complete topological database of all connections in the local network.
RIP takes hop count into consideration but OSPF takes Path Cost into consideration to exchange routing information between the routers.
RIP serves good when small network is taken care of while OSPF is mostly used for large network.

## Slide 9
Thank You